## Slide 1
IF
ID
FE_Latch
RN
ID_Latch
SC
EXE
(Q)
BCAST
SC_Latch
EX_Latch
COMMIT
RAT
REST
ROB
Lab 3: Out of Order Pipeline
LEGEND:
RAT: Register Alias Table
REST: Reservation Station
ROB: ReOrder Bufer
Solid boxes are pipeline stage
Dashed boxes are latches or structures
Boxes in RED to be coded by the students

## Slide 2
New UNIT: Register Alias Table (RAT)
RAT
V
PRF_ID
V
PRF_ID
V
PRF_ID
V
PRF_ID
Each entry has a valid bit and the id of the physical register
In our case, the physical register is embedded in the ROB, so
The RAT maps the destination register to the ROB entry.
If the RAT entry is invalid, then the register is not renamed
And the value can be read from the Architecture Register File
(ARF) right away.
The number of entries in RAT is equal the number of ARF regs.
The RAT needs to provide three functions:
Getting the PRF corresponding to ARF
Setting the PRF for a given ARF entry
Resetting the mapping for a given ARF entry (on retirement)
V
PRF_ID
V
PRF_ID
V
PRF_ID
V
PRF_ID

## Slide 3
New UNIT: Reservation Station (REST)
V
Each entry has a valid bit, scheduled bit, tags for two sources (SRC1tag
And SRC2tag) and if the two inputs are ready.
When a valid entry has both R1 and R2 as true, it can be scheduled. Once
an entry gets scheduled S=1. Note that a scheduled entry does not leave REST.
It leaves the REST only when it finishes execution and is in BCAST stage
The REST needs to provide the following functions:
Check if there is space in the REST
Ability to insert an entry in the REST
Ability to wakeup waiting instructions on a matching broadcast (and mark R=1)
Ability to schedule (changing from S=0 to S=1)
Ability to remove instructions from the REST
REST
S
SRC1tag
SRC2tag
R1
R2

## Slide 4
New UNIT: ReOrder Buffer (ROB)
V
Each entry has a valid bit, ready bit, and instruction info (for destination reg)
The ROB contains a head pointer (pointing to oldest uncommitted instruction) &
a tail pointer (pointing to where a new instruction can be written to)
When a entry is allocated to the ROB, the tail moves. The entry is marked
as valid (V=1) but not ready (R=0). When an instruction completes execution and
Reaches BCAST stage, the ROB entry is marked as ready (R=1). In commit stage, if
the oldest entry is valid and ready, it is removed from the ROB and committed.
The ROB needs to provide the following functions:
Check if there is space in the ROB
Ability to insert an entry in the ROB
Ability to mark the ROB entry as ready (from BCAST stage)
Ability to read a valid and ready ROB entry (from RENAME stage)
Ability to check if the head entry is valid and ready
Remove the head entry if it is valid and ready
ROB
R
InstInfo
HEAD
TAIL

## Slide 5
Known Stages: IF, ID, EX
Instruction FETCH (IF): Responsible for fetching the instruction and passing it to the decode stage. Note that we are assuming perfect branch prediction.
So, we do not need to account for control flow stalls.
Instruction DECODE (ID): Responsible for decoding the instruction and passing it to the rename stage. Note that we are not doing dependency check in this stage.
Dependencies are taken care of later in the pipeline.
Execution Stage (EXE): The EXE stage takes the instruction from the SC_latch and transfers
It to the EX_latch. However, we also need to support multi-cycle instructions. The way we handle this is by having a waiting queue (EXEQ) that buffers waiting instruction and
Tracks their wait times. Once the wait time of the instructions get reduced to zero these
Instructions are transferred to the SC_latch.
NOTE: Our code base will already have the above three stages implemented. So, you will need to focus on implementing only the stages new to the out-of-order pipeline.

## Slide 6
New Stage: Rename (RN) and Reg Read
RN
Need to first check:
Access the ROB to obtain an entry where to place this inst
Access the REST to obtain an entry where to place this inst
If (1) and (2) completes:
Get remapped value of sources using RAT
Update the RAT with destination register remap
If the value can be obtained from the ARF/ROB , mark the sources as ready
Insert instruction in REST

## Slide 7
New Stage: Schedule (SC)
SC
You will implement two scheduling policies:
In order
Check if the oldest instruction in REST is ready (and unscheduled).
If yes, schedule it
If not, stall
Out of Order
Obtain a list of all instructions for which both sources are ready,
And the instruction is unscheduled.
Find the oldest instruction in this list and schedule it

## Slide 8
New Stage: Broadcast(BCAST)
BCAST
The Broadcast stage is responsible for the following:
For all instructions out of the EX stage (note these can be more than pipewidth)
Broadcast the results to all the entries in the REST
This should wake up any sources waiting for this particular tag
Mark the ROB entry as ready
Remove the entry from the reservation station (REST)

## Slide 9
New Stage: COMMIT
COMMIT
The commit stage is responsible for the following:
Check the head of the ROB to see if the head of the ROB is ready
If yes, commit that instruction, update the stats, halt the pipeline if need be
Also, remove the instruction from the ROB, which will increment the ROB head